## Slide 1: Whether the weather be wet Or whether the weather be hot We’ll weather the weather Whatever the weather Whether we like it or not!
Anonymous
(I’m Andrew Trotman)

## Slide 2: Christmas 2013

## Slide 3: USB Wireless Weather Station

## Slide 4: USB Wireless Weather Station
Wind direction
Wind speed
Temperature
Humidity
Cumulative rainfall
Absolute air pressure

## Slide 5: Remote Sensor
Pluviometer
Anemometer
Vane
Thermometer
Hygrometer
Photovoltaic
Transmitter

## Slide 6: Base Unit
Inside temp / humidity
Outside temp / humidity
Guesswork
Current Time / Date
Wind direction
Wind speed
Rain
Air pressure
Guesswork
Memory usage

## Slide 7: Temperature
Thermistor ( )
The relationship between resistance and temperature is (1st order) linear
DR=kDT
k = temperature coefficient of resistance
  If we know R at a given temperature, and we know k then we can solve for T.
The weather station is accurate to 0.1°C For more accuracy (0.02° over 200°C range) the Steinhart–Hart equation is used:
1/T = A+B ln(R)+C(ln(R))3
For more information on thermistors see http://en.wikipedia.org/wiki/Thermistor