## Slide 1: Whether the weather be wet…
“One of the things Ford Prefect had always found hardest to understand about human beings was their habit of continually stating and repeating the obvious, as in It's a nice day, or You're very tall, or Oh dear you seem to have fallen down a thirty-foot well, are you alright? At first Ford had formed a theory to account for this strange behaviour. If human beings don't keep exercising their lips, he thought, their mouths probably seize up. After a few months' consideration and observation he abandoned this theory in favour of a new one. If they don't keep on exercising their lips, he thought, their brains start working. After a while he abandoned this one as well as being obstructively cynical and decided he quite liked human beings after all, but he always remained desperately worried about the terrible number of things they didn't know about.” – Douglas Adams (1979), The Hitchhiker’s Guide to the Galaxy

## Slide 2: Whether the weather be wet Or whether the weather be hot We’ll weather the weather Whatever the weather Whether we like it or not!
Anonymous
(I’m Andrew Trotman)

## Slide 3: Christmas 2013

## Slide 4: USB Wireless Weather Station

## Slide 5: USB Wireless Weather Station
Temperature
Humidity
Cumulative rainfall
Wind speed
Wind direction
Absolute air pressure

## Slide 6: Remote Sensor
Pluviometer
Anemometer
Vane
Thermometer
Hygrometer
Photovoltaic
Transmitter

## Slide 7: Base Unit
Inside temp / humidity
Outside temp / humidity
Magic
Current Time / Date
Wind direction
Wind speed
Rain
Air pressure
Magic
Memory usage

## Slide 8: Thermometer
Thermistor
The relationship between resistance and temperature is (1st order) linear
DR=kDT
k = temperature coefficient of resistance
  If we know R at a given temperature, and we know k then we can solve for T.
The weather station is accurate to 0.1°C For more accuracy (0.02° over 200°C range) the Steinhart–Hart equation is used:
1/T = A+B ln(R)+C(ln(R))3
http://en.wikipedia.org/wiki/Thermistor

## Slide 9: Hygrometer
Probably a capactive humistor
  The dielectric plate of a capacitor is made from a material that absorbs moisture and releases it into the capacitor thus changing its capacitive behavior
  To measure humidity, measure the capacitance of the device
  Modern versions come on a chip that does all the hard work

## Slide 10: Pluviometer
Simple bucket-tipping seesaw mechanism. Each 0.2794 mm of rain causes a tip.
Each “tip” sends a magnet past a reed switch
A microcontroller counts “ticks”
http://bsd.ee/~hadara/blog/?paged=2
http://bsd.ee/~hadara/blog/?paged=2

## Slide 11: Anemometer
As the cups rotate a magnet passes a reed switch and creates a pulse. A microcontroller counts pulses per second. This board (apparently) pulses twice per rotation.
http://www.digitalham.co.uk/weather/equipment/watson-w8681/wind-speed/

## Slide 12: Vane
Digital to analog converter
Reed switches arranged in an octagon
  The magnet is on the “pointer”
When the wind blows at most two switches close
Each switch is connected to a different ohm resister
Measure the voltage drop of the circuit to get direction
http://sandaysoft.com/forum/viewtopic.php?f=13&t=492&start=15

## Slide 13: Barometer
Located in the base station
Piezoresistive
  As the pressure changes the resistivity changes
http://sandaysoft.com/forum/viewtopic.php?f=4&p=5391