## Slide 1: Whether the weather be wet…
“One of the things Ford Prefect had always found hardest to understand about human beings was their habit of continually stating and repeating the obvious, as in It's a nice day, or You're very tall, or Oh dear you seem to have fallen down a thirty-foot well, are you alright? At first Ford had formed a theory to account for this strange behaviour. If human beings don't keep exercising their lips, he thought, their mouths probably seize up. After a few months' consideration and observation he abandoned this theory in favour of a new one. If they don't keep on exercising their lips, he thought, their brains start working. After a while he abandoned this one as well as being obstructively cynical and decided he quite liked human beings after all, but he always remained desperately worried about the terrible number of things they didn't know about.” – Douglas Adams (1979), The Hitchhiker’s Guide to the Galaxy

## Slide 2: Whether the weather be wet Or whether the weather be hot We’ll weather the weather Whatever the weather Whether we like it or not!
Anonymous
(I’m Andrew Trotman)

## Slide 3: Christmas 2013

## Slide 4: USB Wireless Weather Station

## Slide 5: USB Wireless Weather Station
Temperature
Humidity
Cumulative rainfall
Wind speed
Wind direction
Absolute air pressure

## Slide 6: Remote Sensor
Pluviometer
Anemometer
Vane
Thermometer
Hygrometer
Photovoltaic
Transmitter

## Slide 7: Base Unit
Inside temp / humidity
Outside temp / humidity
Magic
Current Time / Date
Wind direction
Wind speed
Rain
Air pressure
Magic
Memory usage

## Slide 8: Thermometer
Thermistor
The relationship between resistance and temperature is (1st order) linear
DR=kDT
k = temperature coefficient of resistance
  If we know R at a given temperature, and we know k then we can solve for T.
The weather station is accurate to 0.1°C For more accuracy (0.02° over 200°C range) the Steinhart–Hart equation is used:
1/T = A+B ln(R)+C(ln(R))3
http://en.wikipedia.org/wiki/Thermistor

## Slide 9: Hygrometer
Probably a capacitive humistor
  The dielectric plate of a capacitor is made from a material that absorbs moisture and releases it into the capacitor thus changing its capacitive behavior
  To measure humidity, measure the capacitance of the device
  Modern versions come on a chip that does all the hard work

## Slide 10: Pluviometer
Simple bucket-tipping seesaw mechanism. Each 0.2794 mm of rain causes a tip.
Each “tip” sends a magnet past a reed switch
A microcontroller counts “ticks”
http://bsd.ee/~hadara/blog/?paged=2
http://bsd.ee/~hadara/blog/?paged=2

## Slide 11: Anemometer
As the cups rotate a magnet passes a reed switch and creates a pulse. A microcontroller counts pulses per second. This board (apparently) pulses twice per rotation.
http://www.digitalham.co.uk/weather/equipment/watson-w8681/wind-speed/

## Slide 12: Vane
Digital to analog converter
Reed switches arranged in an octagon
  The magnet is on the “pointer”
When the wind blows at most two switches close
Each switch is connected to a different ohm resister
Measure the voltage drop of the circuit to get direction
http://sandaysoft.com/forum/viewtopic.php?f=13&t=492&start=15

## Slide 13: Barometer
Located in the base station
Piezoresistive
  As the pressure changes the resistivity changes
http://sandaysoft.com/forum/viewtopic.php?f=4&p=5391

## Slide 14: Wire It Up

## Slide 15: Screw It Up

## Slide 16: Wireless Protocol
10 byte packet sent every 48 seconds at 433 MHz
  Device identifier
  Temperature
  Humidity
  Average wind speed
  Gust wind speed
  Rainfall counter
  Battery indicator
  Wind direction
  Checksum

## Slide 17: Base Station

## Slide 18: USB Wireless Weather Station
The base station can be connected to a PC
  Via USB
Software provided on CD-ROM

## Slide 19: EasyWeather
http://proweatherstation.com/easyweather/easyweather.htm

## Slide 20: EasyWeather
http://proweatherstation.com/easyweather/easyweather.htm

## Slide 21: What I Want (Requirements)
The weather without leaving bed
  Weather on my iPhone
Not “24 hour high”
  Preferred “today vs yesterday”
    Is it warmer today than yesterday?
    How much rain did have we had today?
    Is the barometric pressure going up or down?
Human readable interpretations
Short-term weather forecasting
  (will I need my coat today)

## Slide 22: Hacking the USB Protocol
USB HID device
  Plug it in to a USB port
  lsusb
  “WH1080 Weather Station / USB Missile Launcher”
Luckily others had already hacked the protocol
  It’s a Fine Offset WH1080 (in a DIGITECH box)
  http://code.google.com/p/weatherpoller/wiki/USBProtocol
  http://www.jim-easterbrook.me.uk/weather/mm/

## Slide 23: i.MX6Q
Our i.MX6Q board is also USB HID
  We I have some experience with HID
Open a connection
Sent a “report request”
Receive a “report”

## Slide 24: WH1080 USB HID Protocol
I send 8 bytes (1 x USB 1.0 packet)
  The device has 64KB “RAM”
Byte | Value | Meaning
0 | 0xA1 | READ
1 | AddrHi | High byte of address
2 | AddrLo | Low byte of address
3 | 0x20 | End of message
4 | 0xA1 | READ
5 | AddrHi | High byte of address
6 | AddrLo | Low byte of address
7 | 0x20 | End of message

## Slide 25: WH1080 USB HID Protocol
Device responds with 32-bytes
Byte | Meaning
0 | Minutes since previously stored reading
1 | Base station humidity (%)
2-3 | Base station temperature (x * 0.1 = °C)
4 | Remote sensor humidity (%)
5-6 | Remote sensor temperature (x * 0.1 = °C)
7-8 | Absolute pressure (x/10 = hPa)
9 | Average wind speed (low byte) (x * 0.1 = m/s)
10 | Gust wind speed (log byte) (x * 0.1 = m/s)
11 | Wind speed high byte (top nybble=gust, bottom nybble = average)
12 | Wind direction (x * 22.5 = angle ° from north)
13-14 | Rain bucket “fullness” (x*.3 = mm)
15 | Status (bit 7 = bucket overflow, bit6 = can’t reach remote sensors)

## Slide 26: WH1080 USB HID Protocol
First 256 bytes are “special” and includes
  Device unique ID
  Sample rate (minutes between stored readings)
  Number of stored readings
  Address of current reading
  A load of max, min, display, and alarm settings
Can store 4080 readings in 64KB
  85 days at one reading every 30 minutes
    There is a USD HID write report to reset stuff (see references)

## Slide 27: Hack Time (Exploration)
Web cgi/bin app (on my Windows laptop)
  Temperature, humidity, average wind speed, gust wind speed, wind angle, rainfall, absolute pressure
  Hourly rainfall: get three readings and subtract the first from the third (similarly for 24 hour)
  Wind direction: divide by 22.5 and table lookup
What else…

## Slide 28: Wind Strength (Beaufort Scale)
Invented in 1805 by Rear Admiral Sir Francis Beaufort and first used on HMS Beagle
13 point scale (0..12)
  Qualitative wind conditions to effects on sails, from “just sufficient to give steerage” to “that which no canvas sails could withstand”
1946
  V = 0.836 X B3/2 m/s
This is where “force 10 winds” comes from
  Calm, Light air, Light breeze, Gentle breeze, Moderate breeze, Fresh breeze, Strong breeze, Moderate gale, Gale, Strong gale, Storm, Violent storm, Hurricane
  For Hurricanes use the Saffir–Simpson wind scale

## Slide 29: Apparent Temperature
Wind chill
  When T < 10°C and V > 4.8 km/h
  Developed by the Joint Action Group for Temperature Indices (JAG/TI)
  In use in US, UK, Canada from 2001
  Computed from model of skin heat transfer assuming bare face, facing the wind, and walking at 5 km/h
  Ta = 13.12 + 0.6215T – 11.37V0.16 + 0.3965TV0.16
Somewhat controversial

## Slide 30: Apparent Temperature
Heat index
  Steadman, R. G., 1979 J. Appl. Meteor., 18, 861–885.
  When humidity is high perspiration is less effective
    So It feels hotter
  When T > 27°C, H > 40%, DewPoint > 12°C
  Assuming in shade with no wind
  Compute from a model including 20 parameters such as skin, clothing, temperature, humidity, activity, etc.
  Ta = c1 + c2T + c3R + c4TR + c5T2 + c6R2 + c7T2R + c8TR2 + c9T2R2

## Slide 31: Dew Point
“The dew point is the temperature at which the water vapor in air at constant barometric pressure condenses into liquid water at the same rate at which it evaporates” (Dew point (visited 2014) Wikipedia)
In other words, if the temperature gets lower than the dew point water condenses

## Slide 32: Weather Forecasting
Negretti & Zambra (1915) Zambretti Forcaster
  3 disk system using
  Wind direction
  Sea level adjusted barometric pressure
  Barometric direction (rising, falling, steady)
  Season (summer / winter)
  Adjusted to include:
    Earth Hemisphere
      Direction of equator (warmer wind)
http://www.meteormetrics.com/zambretti.htm

## Slide 33: Zambretti Forcasts
Settled fine
Fine weather
Becoming fine
Fine becoming less settled
Fine, poss showers
Fairly fine, improving
Fairly fine, poss showers early
Fairly fine, showery later
Showery early, improving
Changeable, mending
Fairly fine, showers likely
Rather unsettled clearing later
Unsettled, prob improving
Showery, bright intervals
Showery, becoming more unsettled
Changeable, some rain
Unsettled, short fine intervals
Unsettled, rain later
Unsettled, rain at times
Very unsettled, finer at times
Rain at times, worse later
Rain at times, becoming v. unsettled
Rain at frequent intervals
Very unsettled, rain
Stormy, poss improving
Stormy, much rain

## Slide 34: What else?
Sunrise / sunset
Moon phase

## Slide 35: Finished Web App
Sunrise
Sunset
24 Hour low
24 Hour high
Phase of moon
Time and Date (now)
Wind Direction
Wind speed
Beaufort scale
Humidity
Hourly total rain
24 hour total rain
Temperature
Temperature change
Apparent temperature
Sea level adjusted pressure
Pressure change
Base station details
Forecast
Dew point
Magic
Refresh
Graphs